Digitising a signal

This signal needs to be digitised to store on a computer.  You will look at the effect of sampling rate and signal resolution on the quality of the reconstructed “digitised” signal.

| Time (s) | Signal Value (V) |
| --- | --- |
| 0.00 |  |
| 0.05 |  |
| 0.10 |  |
| 0.15 |  |
| 0.20 |  |
| 0.25 |  |
| 0.30 |  |
| 0.35 |  |
| 0.40 |  |
| 0.45 |  |

- Take samples every 0.05 seconds

- Read the value of the signal to the nearest 0.2V

- Plot the signal on graph paper to show the “reconstructed” signal after digitisation.

Questions:

- What is the sampling rate in Hz?

- How many “levels” are there?

- How many “bits” would be required to store this number of levels?

- What would the binary values be for each signal level?  Write them by the voltages on your graph.

Now repeat each of the above steps and questions:

- Taking samples every 0.05 seconds and reading the signal to the nearest 0.1V

- Taking samples every 0.02 seconds and reading the signal to the nearest 0.2V

- Taking samples every 0.02 seconds and reading the signal to the nearest 0.1V