Year 12 – Imaging starter questions

- Explain what is meant by:

  - A pixel

  - The resolution of an image

  - The number of levels in an image

  - A false colour image

- A CCD sensor measures 1920×2184 pixels (horizontal×vertical).  Each cell in the ccd is capable of detecting 16.7million colours.

  - How many bits is required to store each pixel?

  - What is the total amount of information stored in the image in bytes.

- An ultraviolet image of the sun is stored using 16bits per pixel.

  - How many levels are in the image?  Show your working.

  - Why is it not correct to say this is the number of colours in the image?

  - If the image is 3072 × 3072 pixels, how much total data is required to store the image?  Give your answer in a convenient unit.

  - Calculate the resolution, given that the image of the sun fills the whole array, and the diameter of the sun is 1.39×106 km.  Draw a sketch to help you solve this problem.

- A particular digital SLR camera is fitted with a wide angle lens of focal length 28mm.

  - What distance must the lens be from the CCD sensor to focus a distant object?  Draw a sketch and explain your answer.

  - What is the power of the lens?

  - What is the curvature of waves reaching the lens from an object at a distance of 40cm?

  - What is the curvature of these waves after the lens has added its curvature to them?

  - What distance must the lens be from the CCD to focus an object at this distance?  Draw a sketch to help you solve this problem.

  - How far has it moved from its position when focusing a distant object?

- Pixels in a particular image are stored using 8bits per pixel.

  - A particular pixel has a decimal value of 41.  Give the sequence of bits representing this pixel.

  - Another pixel has a decimal value of 115.  Give the sequence of bits representing this pixel.

  - Explain why a pixel in this image could not have a value of 320.  Use a calculation or numerical example to support your answer.

Year 12 – Imaging starter questions

- Explain what is meant by:

- A pixel

- The resolution of an image

- The number of levels in an image

- A false colour image

- A CCD sensor measures 1920×2184 pixels (horizontal×vertical).  Each cell in the ccd is capable of detecting 16.7million colours.

- How many bits is required to store each pixel?

- What is the total amount of information stored in the image in bytes.

- An ultraviolet image of the sun is stored using 16bits per pixel.

- How many levels are in the image?  Show your working.

- Why is it not correct to say this is the number of colours in the image?

- If the image is 3072 × 3072 pixels, how much total data is required to store the image?  Give your answer in a convenient unit.

- Calculate the resolution, given that the image of the sun fills the whole array, and the diameter of the sun is 1.39×106 km.  Draw a sketch to help you solve this problem.

- A particular digital SLR camera is fitted with a wide angle lens of focal length 28mm.

- What distance must the lens be from the CCD sensor to focus a distant object?  Draw a sketch and explain your answer.

- What is the power of the lens?

- What is the curvature of waves reaching the lens from an object at a distance of 40cm?

- What is the curvature of these waves after the lens has added its curvature to them?

- What distance must the lens be from the CCD to focus an object at this distance?  Draw a sketch to help you solve this problem.

- How far has it moved from its position when focusing a distant object?

- Pixels in a particular image are stored using 8bits per pixel.

- A particular pixel has a decimal value of 41.  Give the sequence of bits representing this pixel.

- Another pixel has a decimal value of 115.  Give the sequence of bits representing this pixel.

- Explain why a pixel in this image could not have a value of 320.  Use a calculation or numerical example to support your answer.