Finding the resistivity of a material

Resistivity is a property of a material that defines its ability to resist the flow of an electric current. The length and CSA of the material also determine its resistance.

Resistance = Resistivity x Length

CSA

R = ρ X L		Ω = Ω.m  x  m

A			    m2

To find the resistivity of nichrome wire:

| Length (m) | Current (A) | Voltage (V) | Resistance (Ω) |
| --- | --- | --- | --- |
| 1.00 0.90 0.80 |  |  |  |

Diameter = ……….mm

Radius = ……….. mm  = …………….m

CSA = πr2  = 3.14 x (                 )2    = ………………….. m2

A graph of Resistance (y axis)  v Length (x axis) should have a gradient of ρ/A. Therefore find the gradient and multiply it by the CSA to find the resistivity.

Repeat for copper wire.

Compare your values with those given in the Materials Database.