How the electron deflection tube works

Calculating the size of the deflecting force

# Text boxes

Low voltage ac

heated wire coil

High voltage electrode

+4000V

+ + + + + +

+ + + + + +

electrons gain sufficient thermal energy to escape from the surface of the heated wire coil and are accelerated toward the high voltage electrode.

Electrons have gained kinetic energy.

The electron enters the uniform electric field between the deflection plates.

–	–	–	–	–	–	–	–	–

+	+	+	+	+	+	+	+	+

Electrons leave with

Value of Ek = ____________

Value of v = _____________

Strength of field is given by

Where:

V is voltage between plates

d is separation of plates

Value of E =

Electron travels distance Δx between plates

deflected by distance Δy

+	+	+	+	+	+	+	+	+

–	–	–	–	–	–	–	–	–

The electron takes some time t to traverse distance Δx

During this time it is accelerated in the y-direction, such that it is deflected by a distance Δy

Value of t = _______________

It follows that the acceleration can be calculated from

The initial velocity, uy is zero in the y direction so we have

which rearranges to give

Value of sy = _________	Value of ay = _________

Now we know that the acceleration must be caused a force and that this force is due to the deflecting electric field.

It is obvious that the magnitude of the accelerating force must be:

Value of Fy = ___________

This force has been provided by the electric field.  We know that the electric field E is defined as the force per unit charge, such that:

So the value of the force we have calculated by using the equations of motion, combined with Newton’s 3rd law, should be equal to:

value of F = ___________________

if we have performed all our calculations correctly…!

Are the values approximately equal…?		Yes   /   No